## Slide 1: What you need:
Project guide
Apparent Brightness with Energy Light Meter
Integrating CS with Science - 5th Grade
Light source

## Slide 2: Apparent Brightness with Energy Light Meter
Summary & Context
The BBC micro:bit has a light sensor on its LED display which can be used to explore light levels at different distances from a light source.
Building on this, you can use the micro:bit and a light source to create a model demonstrating the apparent brightness of objects in space based on their relative distance from Earth. Students can then create a scientific argument based on their observation of the model.
This activity requires a light source.
micro:bit Feature: Light Sensor
The micro:bit can be programmed to use its LED display as a light sensor. It measures light strength from 0 (no light) to 255 (very bright light).
Example: Students can measure the brightness of a light source by taking measurements at different distances near and far from the source.

## Slide 3: Computer Science Concepts
Inputs
Inputs allow computers to sense things happening in the real world so they can act on them and make something happen.
This project uses the light sensor and buttons for input.
The micro:bit has two buttons which can be programmed – buttons A and B. This project uses button A to measure light levels and store them in a variable. Button B is used to view the most recent measurement taken.
Storing Data
Variables store numbers or values that can change in a computer program.
We can describe variables as being like a box that stores information and which students can access, add to, or remove from at any time.
In computer science, a ‘string’ is a sequence of characters that can contain letters, numbers, symbols, and spaces.

## Slide 4: How the Energy Light Meter Works
The energy light meter uses a variable called “reading” to store the light level measured. It uses the micro:bit light sensor to store the light level in this variable when the program starts.
Students press button A each time they want to measure a light level.
Students press button B each time they want to view the most recent light level measured.
Using a variable to store the light level, rather than just displaying it, is helpful because students can take a light reading in a place where the display may be difficult to see, then wait to view the light measurement in a more convenient place.
Pro tip: You need a room that you can make dark to simulate space. Your light source will represent the sun.

## Slide 5: Pick Your Level
Mild 🌶️ 30 mins | Learning outcome: I can collect light level data at different distances from the light source using the micro:bit energy light meter.
 | Activity description: Using existing code and a light source to simulate the sun, measure light levels at different distances near and far from the source.
Medium 🌶️🌶️ 45 mins | Learning outcome: I can modify my own energy light meter program to collect accurate light level data.
 | Activity description: Modify the starter project to code your own light meter to measure light levels at different distances near and far from the source.
Spicy 🌶️🌶️🌶️ 45-60 mins | Learning outcome: I can create my own energy light level program to collect accurate light level data.
 | Activity description: Code your own light meter program to measure light levels at different distances near and far from the source.

## Slide 6
Mild

## Slide 7: Mild 🌶️ Introduction 1
Students will download the code on their micro:bit, connect the battery pack, measure the brightness of a light source at different distances, and record their data.
Place a light source (lamp, lantern) in a room where you can turn off all other lights and block out daylight during data collection. Teachers may wish to identify measurement spots in the classroom if results are being compared between students. Measurement spots should be at different distances near and far from the source.
The micro:bit’s light sensor uses the display LEDs to measure light, so make sure the micro:bit’s LED display is pointing toward the light source. The light level reading will be a number between 0 (dark) and 255 (the most intense light the micro:bit can measure).
Mild 🌶️ - Medium - Spicy

## Slide 8: Mild 🌶️ Introduction 2
Students can use button B to display their light level reading, record it, and prepare to collect data at a different measurement spot.
  The apparent brightness recording sheet can be used to record the distance from the light source and light level reading in each spot.
  Variables hold one value at a time. Students should record distance from the light source and light level on the sheet after each measurement.
After collecting the data, students can create graphs to support class discussion about how the apparent brightness of the sun compares to other stars based on their relative distances from Earth.
Mild 🌶️ - Medium - Spicy

## Slide 9: Mild 🌶️ Student Activity Steps
Open the project: mbit.io/us-lightmeter and download the code to the micro:bit.
Unplug the micro:bit and connect the battery pack.
Go to a measurement spot and start collecting data.
Collect light level data by pressing button A.
Press button B on micro:bit to show the light level data on the LED display.
Record distance from the light source and light level on a worksheet.
Repeat data collection at different measurement spots and discuss distance and light level measurements. What do students notice and wonder about their results?
Mild 🌶️ - Medium - Spicy

## Slide 10: Mild 🌶️ Code Details
This project measures light level from 0 (darkest) to 255 (brightest).
Mild 🌶️ - Medium - Spicy
At the start of the program, the LED display shows “M” to signal that the micro:bit is ready to measure light levels, stores the initial light measurement in variable “reading” and pauses for 100 ms before another input can happen.
Pressing button A measures the light level and stores it in variable “reading”. The LED display shows an animation to signal that a measurement was made and then waits half a second (500 ms) before showing “M” for measure.
Pressing button B will clear the screen, show the light level stored in the variable “reading” on the LED display, and wait half a second (500 ms) before showing “M” on the LED display.

## Slide 11
Medium

## Slide 12: Medium 🌶️🌶️ Introduction 1
Students open a starter project containing all the blocks they need to make the project.
Place a light source (lamp, lantern) in a room where you can turn off all other lights and block out daylight during data collection. Teachers may wish to identify measurement spots in the classroom if results are being compared between students. Measurement spots should be at different distances near and far from the source.
The micro:bit’s light sensor uses the LEDs in its display to measure light, so make sure the micro:bit’s LED display is pointing toward the light source. The light level reading will be a number between 0 (dark) and 255 (the most intense light the micro:bit can measure).
Mild - Medium 🌶️🌶️ - Spicy

## Slide 13: Medium 🌶️🌶️ Introduction 2
Students can use button B to display their light level reading, record it, and prepare to collect data at a different measurement spot.
  The apparent brightness recording sheet can be used to record the distance from the light source and light level reading in each spot.
  Variables hold one value at a time. Students should record distance from the light source and light level on the sheet after each measurement.
After collecting the data, students can create graphs to support class discussion about how the apparent brightness of the sun compares to other stars based on their relative distances from Earth.
Mild - Medium 🌶️🌶️ - Spicy

## Slide 14: Medium 🌶️🌶️ Student Activity Steps 1
Build the code:
Open the starter project: mbit.io/us-lightmeter-pp
Explain that students have all the code blocks they need.
Code the program to start with showing ‘M’ for measure, set variable “reading” to store the light level measured, and pause for 100 ms before adding another input.
Make sure student code looks like:
Discuss the importance of accurate data and why it is helpful to pause before adding another input.
Mild - Medium 🌶️🌶️ - Spicy

## Slide 15: Medium 🌶️🌶️ Student Activity Steps 2
Build the code - part 2:
Code Button A to measure the light level and store it in variable “reading”, show an animation to help students know a measurement was made, and then wait half a second (500 ms) before showing ‘M’ for measure.
Make sure student code looks like:
Mild - Medium 🌶️🌶️ - Spicy

## Slide 16: Medium 🌶️🌶️ Student Activity Steps 3
Build the code - part 3:
Code Button B to clear the screen, show the light level stored in “reading”, and wait half a second (500 ms) before showing ‘M’ for measure.
Make sure student code looks like:
Test their code using the simulator and then download the code to their micro:bit.
Mild - Medium 🌶️🌶️ - Spicy

## Slide 17: Medium 🌶️🌶️ Student Activity Steps 4
Mild - Medium 🌶️🌶️ - Spicy
Use your micro:bit to collect data:
Unplug the micro:bit and connect the battery pack.
Go to a measurement spot and start collecting data.
Collect light level data by pressing Button A.
Press button B on micro:bit to show the light level data on the LED display.
Record distance from the light source and light level on a worksheet.
Repeat data collection at different measurement spots and discuss distance and light level measurements. What do students notice and wonder about their results?

## Slide 18: Medium 🌶️🌶️ Code Details
This project measures light level from 0 (darkest) to 255 (brightest).
At the start of the program, the LED display shows “M” to signal that the micro:bit is ready to measure light levels, stores the initial light measurement in variable “reading” and pauses for 100 ms before another input can happen.
Pressing button A measures the light level and stores it in variable “reading”. The LED display shows an animation to signal that a measurement was made and then waits half a second (500 ms) before showing “M” for measure.
Pressing button B will clear the screen, show the light level stored in the variable “reading” on the LED display, and wait half a second (500 ms) before showing “M” on the LED display.
Mild - Medium 🌶️🌶️ - Spicy

## Slide 19
Spicy

## Slide 20: Spicy 🌶️🌶️🌶️ Introduction 1
Mild - Medium - Spicy 🌶️🌶️🌶️
Students open Microsoft MakeCode and code their own energy light meter.
Place a light source (lamp, lantern) in a room where you can turn off all other lights and block out daylight during data collection. Teachers may wish to identify measurement spots in the classroom if results are being compared between students. Measurement spots should be at different distances near and far from the source.
The micro:bit’s light sensor uses the LEDs in its display to measure light, so make sure the micro:bit’s LED display is pointing toward the light source. The light level reading will be a number between 0 (dark) and 255 (the most intense light the micro:bit can measure).

## Slide 21: Spicy 🌶️🌶️🌶️ Introduction 2
Mild - Medium - Spicy 🌶️🌶️🌶️
Students can use button B to display their light level reading, record it, and prepare to collect data at a different measurement spot.
  The apparent brightness recording sheet can be used to record the distance from the light source and light level reading in each spot.
  Variables hold one value at a time. Students should record distance from the light source and light level on the sheet after each measurement.
After collecting the data, students can create graphs to support class discussion about how the apparent brightness of the sun compares to other stars based on their relative distances from Earth.

## Slide 22: Spicy 🌶️🌶️🌶️ Student Activity Steps 1
Build the code:
Open Microsoft MakeCode microbit.makecode.org
Explain that students will use the toolbox to find code blocks.
Explain that students will need to code the three parts of the energy light meter:
  Code the program to show ‘M’ for measure, set variable “reading” to store the light level measured, and pause for 100 ms on start.
  Code Button A to measure the light level and store it in variable “reading”, show an animation to help students know a measurement was made, and then wait half a second (500 ms) before showing ‘M’ for measure.
  Code Button B to clear the screen, show the light level stored in “reading”, and wait half a second (500 ms) before showing ‘M’ for measure.
Mild - Medium - Spicy 🌶️🌶️🌶️

## Slide 23: Spicy 🌶️🌶️🌶️ Student Activity Steps 2
Build the code - on start:
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘show string’ block in the Basic section and update the string to read M to help students know the micro:bit is ready to measure light levels.
Select ‘Make a Variable’ in the Variables section. Name your variable “reading” because it will store the most recent light level recorded. You will see two new variable blocks appear.
Pro tip: It’s best to use variable names that describe the information that will be stored instead of using single letters like x, y, or z.

## Slide 24: Spicy 🌶️🌶️🌶️ Student Activity Steps 3
Build the code - on start part 2:
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘pause’ block in the Basic section to add a 100 ms pause before another input can happen.
Find the ‘set reading to 0’ block in the Variables section.
Find the ‘light level’ block in the Input section and put it on top of the 0 in ‘set reading to 0’ block. This will store the current light level reading in variable “reading”.

## Slide 25: Spicy 🌶️🌶️🌶️ Student Activity Steps 4
Build the code - Button A:
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘on button A pressed’ block in the Input section and add it to your workspace.
Find the ‘set reading to 0’ block in the Variables section.
Find the ‘light level’ block in the Input section and put it on top of the 0 in ‘set reading to 0’ block. This will store the current light level reading in variable “reading” when button A is pressed.

## Slide 26: Spicy 🌶️🌶️🌶️ Student Activity Steps 5
Build the code - Button A part 2:
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘show icon’ block in the Basic section and select the arrow to the right of the heart icon image and select the ‘small diamond’ icon.
Find the ‘show icon’ block in the Basic section and select the arrow to the right of the heart icon image and select the ‘diamond’ icon.
Find the ‘show string’ block in the Basic section and update the string to read M to help students know the micro:bit is ready to measure light levels.

## Slide 27: Spicy 🌶️🌶️🌶️ Student Activity Steps 6
Build the code - Button B:
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘show number 0’ block in the Input section.
Find variable “reading” in the Variables section and put it on top of the 0 in “show number 0’ block.
Find the ‘on button A pressed’ block in the Input section and add it to your workspace. Select the down arrow and select B.
↓
Find the ‘clear screen’ block in the Basics section.

## Slide 28: Spicy 🌶️🌶️🌶️ Student Activity Steps 7
Build the code - Button B part 2:
Test their code using the simulator and then download the code to their micro:bit.
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘pause’ block in the Basics section and click the arrow to update to time to one half second (5000 ms).
Find the ‘show string’ block in the Basic section and update the string to read M to help students know the micro:bit is ready to measure light levels.

## Slide 29: Spicy 🌶️🌶️🌶️ Student Activity Steps 8
Mild - Medium - Spicy 🌶️🌶️🌶️
Use your micro:bit to collect data:
Unplug the micro:bit and connect the battery pack.
Go to a measurement spot and start collecting data.
Collect light level data by pressing Button A.
Press button B on micro:bit to show the light level data on the LED display.
Record distance from the light source and light level on a worksheet.
Repeat data collection at different measurement spots and discuss distance and light level measurements. What do students notice and wonder about their results?

## Slide 30: Spicy 🌶️🌶️🌶️ Code Details
This project measures light level from 0 (darkest) to 255 (brightest).
At the start of the program, the LED display shows “M” to signal that the micro:bit is ready to measure light levels, stores the initial light measurement in variable “reading” and pauses for 100 ms before another input can happen.
Pressing button A measures the light level and stores it in variable “reading”. The LED display shows an animation to signal that a measurement was made and then waits half a second (500 ms) before showing “M” for measure.
Pressing button B will clear the screen, show the light level stored in the variable “reading” on the LED display, and wait half a second (500 ms) before showing “M” on the LED display.
Mild - Medium - Spicy 🌶️🌶️🌶️

## Slide 31
Extension Ideas

## Slide 32: Energy Light Meter Extensions
Add a second micro:bit and radio functionality to allow remote reading of light levels.
If you have access to a light meter that measures light levels in other units, compare the micro:bit's readings with it.
Model apparent brightness by programming multiple micro:bits with varying brightness based on the distance from Earth.