## Slide 1
What you need:
Project guide
Data-based Solutions with Environment Data Logger
Integrating CS with Science - 5th Grade
Outdoor space

## Slide 2: Community Data Collection with Environment Data Logger
Summary & Context
Students can use the BBC micro:bit to collect environment data (temperature and light) over time and combine their data with community-based environmental protection data and protection measures.
Students can also use the micro:bit to design and engineer solutions to protect resources in their community (for example water, renewable energy).
Consider working with local experts to create connections between collecting data and designing solutions using science ideas.
micro:bit Feature: Temperature Sensor
The micro:bit has a temperature sensor inside its processor which can give an approximation of the air temperature.
Example: Program the micro:bit to measure the approximate temperature around you.

## Slide 3: Computer Science Concepts
Variables
Variables store numbers or values that can change in a computer program.
We can describe variables as being like a box that stores information and which students can access, add to, or remove from at any time.
Boolean variables are a specific type of variable that can only have two values, true or false.
This program uses a boolean variable called “logging” that determines when the micro:bit logs data.
Infinite Loop
Loops tell the computer to do an instruction (or set of instructions) over and over again. There are different types of loops, including infinite, count-controlled, and condition-controlled loops.
This program uses an infinite loop (‘every 60,000 ms’ block), which instructs the micro:bit check if the micro:bit is logging data every minute.

## Slide 4: How the Environment Data Logger Works
The program uses a logging variable, which can be set to “true” or “false”.
Press button A to start logging. A checkmark will appear on the LED display and data will be recorded every minute.
A heart flashes on the LED display to signal when data is being recorded.
Press button B to stop logging. You’ll see an X appear to signal the micro:bit has stopped logging.
Press buttons A and B together to delete all data. A skull icon will appear on the LED display.
In the unlikely event the log becomes full, the micro:bit lights all the LEDs on the display.
Pro Tip: If you are leaving your micro:bits outside, place them in sealed clear plastic bags so they don’t get wet. Water can damage your micro:bits. Use new batteries in your battery packs to log for longer periods of time.

## Slide 5: Pick Your Level
Mild 🌶️ 30 mins | Learning outcome: I can collect environmental data over time using the micro:bit environment data logger and combine it with information from my community to design solutions that help protect the local environment.
 | Activity description: Using existing code, collect temperature and light data over time. Combine data collected with similar data collected by community-based organizations to help students design solutions to protect the local environment.
Medium 🌶️🌶️ 45 mins | Learning outcome: I can modify my own environment data logger program to collect environmental data over time, combine it with community data, and design solutions to protect the local environment.
 | Activity description: Modify the starter project to code your own environment data logger to collect temperature and light data over time. Combine data collected with similar data collected by community-based organizations to help students design solutions to protect the local environment.
Spicy 🌶️🌶️🌶️ 45-60 mins | Learning outcome: I can create my own environment data logger program to collect environmental data over time, combine it with community data, and design solutions to protect the local environment.
 | Activity description: Code your own environment data logger to collect temperature and light data over time. Combine data collected with similar data collected by community-based organizations to help students design solutions to protect the local environment.

## Slide 6
Mild

## Slide 7: Mild 🌶️ Introduction 1
Students will download the code on their micro:bit, attach a battery pack, take it to the area they want to test, and start data logging.
Remember to identify the areas where students will be collecting data. Select areas with varying light and temperature levels to encourage interesting discussions.
Students will return to the area later to stop data logging and collect their micro:bits.
Students will connect their micro:bits to a computer or tablet to download the data collected. They can then view the data and graphs generated from their data logging on a webpage. They can also plot their own graphs from the data collected.
Mild 🌶️ - Medium - Spicy

## Slide 8: Mild 🌶️ Introduction 2
The micro:bit’s light sensor uses the display LEDs to measure light, so make sure the micro:bit’s LED display is pointing toward the light source. The light level reading will be a number between 0 (dark) and 255 (the most intense light the micro:bit can measure).
The temperature sensor is in the processor on the back of the micro:bit and provides a good approximation of the temperature around the device. It is important to remember that items touching the processor or
a person holding the micro:bit can impact the temperature reading, so students should not pick up the micro:bit to take readings. This project is programmed to display the temperature reading in Fahrenheit.
Mild 🌶️ - Medium - Spicy

## Slide 9: Mild 🌶️ Student Activity Steps 1
Open the project: mbit.io/us-environment and download the code to the micro:bit.
Unplug the micro:bit and connect the battery pack.
Place your micro:bit in the predetermined observation area.
Start data logging by pressing button A. Leave the micro:bit logging for a period of time.
Return to the micro:bit and press button B to stop logging.
Disconnect the battery pack and plug the micro:bit back into a computer.
Mild 🌶️ - Medium - Spicy
Pro Tip: Be sure to connect the micro:bit to a computer and save the MY_DATA file before pressing buttons A and B together to delete all data.

## Slide 10: Mild 🌶️ Student Activity Steps 2
The MICROBIT drive will appear like a USB drive.
Look in the MICROBIT drive and open the MY_DATA file to see a table of your data in a web browser.
Mild 🌶️ - Medium - Spicy
↓

## Slide 11: Mild 🌶️ Student Activity Steps 3
Click the Visual preview button to see a graph of your data.
You can also click the Copy button and then paste your data into a spreadsheet.
Mild 🌶️ - Medium - Spicy

## Slide 12: Mild 🌶️ Analyze Your Data 1
Your data appears in a table in the web browser.
Mild 🌶️ - Medium - Spicy
The time stamps in the log represent the amount of time that has passed since your micro:bit was powered on. If you log more than one set of data without clearing the log, you may not be able to see the visual preview of the data you want to study, so it’s a good idea to delete the previously stored log before starting a new experiment.

## Slide 13: Mild 🌶️ Analyze Your Data 2
Click the Visual preview button above the data table to see a graph of your data:
The light and temperature data are logged and displayed within different number ranges. Click the labels to view a single data type in more detail with an appropriately scaled graph.
You can also click the Copy button and then paste your data into a spreadsheet.
Mild 🌶️ - Medium - Spicy

## Slide 14: Mild 🌶️ Code Details 1
This project uses a Boolean variable, which can only store one of two values - true or false. The Boolean variable is called “logging”, and it controls when the micro:bit logs data.
Mild 🌶️ - Medium - Spicy
When the program starts, the variable “logging” is set to false. An X icon is displayed to signal that data is not being logged. The data collection categories are organized in columns and named “temperature” and “light” for this project.
Pressing button A sets the variable “logging” to true and displays a checkmark to signal that data logging is happening. Pressing button B sets “logging” to false and displays an X to signal that data logging has ended.

## Slide 15: Mild 🌶️ Code Details 2
Mild 🌶️ - Medium - Spicy
This program uses an infinite loop, the ‘every 60,000 ms’ block, that checks if the micro:bit is logging data every minute.
If the micro:bit is logging, it shows a heart on its LED display, records (logs) the temperature and light level data in the appropriate column, and then clears the display to signal that data logging is complete every minute.

## Slide 16: Mild 🌶️ Code Details 3
Mild 🌶️ - Medium - Spicy
The micro:bit's temperature sensor measures in Celsius.
The ‘convertCtoF function’ converts the temperature from Celsius to Fahrenheit by multiplying it by 1.8 and adding 32. Using a function to convert the temperature allows you to re-use the conversion code every time data is logged.
The function is used with the ‘call convertCtoF “temperature (℃)” ‘ block found within the infinite loop block of code.

## Slide 17: Mild 🌶️ Code Details 4
Pressing buttons A + B together will delete all data in the log. The LED displays a skull icon to signal that data is erased, the ‘delete log’ block erases all data, and the data collection categories are assigned “temperature” and “light” so the micro:bit is ready to collect data the next time button A is pressed.
Mild 🌶️ - Medium - Spicy
While unlikely, it is possible for the log to be full. When this happens, the variable “logging” is set to false and the full LED display lights up to signal that the log is full.

## Slide 18
Medium

## Slide 19: Medium 🌶️🌶️ Introduction 1
Mild - Medium 🌶️🌶️ - Spicy
Students will download the code on their micro:bit, attach a battery pack, take it to the area they want to test, and start data logging.
Remember to identify the areas where students will be collecting data. Select areas with varying light and temperature levels to encourage interesting discussions.
Students will return to the area later to stop data logging and collect their micro:bits.
Students will connect their micro:bits to a computer or tablet to download the data collected. They can then view the data and graphs generated from their data logging on a webpage. They can also plot their own graphs from the data collected.

## Slide 20: Medium 🌶️🌶️ Introduction 2
Mild - Medium 🌶️🌶️ - Spicy
The micro:bit’s light sensor uses the display LEDs to measure light, so make sure the micro:bit’s LED display is pointing toward the light source. The light level reading will be a number between 0 (dark) and 255 (the most intense light the micro:bit can measure).
The temperature sensor is in the processor on the back of the micro:bit and provides a good approximation of the temperature around the device. It is important to remember that items touching the processor or
a person holding the micro:bit can impact the temperature reading, so students should not pick up the micro:bit to take readings. This project is programmed to display the temperature reading in Fahrenheit.

## Slide 21: Medium 🌶️🌶️ Student Activity Steps 1
Build the Code - part 1:
Open the starter project: mbit.io/us-environment-pp
Explain that students have all the code blocks they need and explain that some of the code has already been built for them.
Explain that they will be building their own environment data logger.
Use the ‘on button A pressed’ block to set logging to true and show a checkmark icon.
Use the ‘on button B pressed’ block to set logging to false and show an X icon.
Make sure student code looks like:
Mild - Medium 🌶️🌶️ - Spicy

## Slide 22: Medium 🌶️🌶️ Student Activity Steps 2
Build the Code - part 2:
Use the ‘on button A + B’ block to delete the log and show a skull icon indicating data has been deleted.
Use the ‘set columns’ block to ensure the micro:bit adds the column headings “temperature” and “light” to your new data table.
Make sure student code looks like:
Test their code using the simulator and then download the code to their micro:bit.
Mild - Medium 🌶️🌶️ - Spicy

## Slide 23: Medium 🌶️🌶️ Student Activity Steps 3
Use Your micro:bit to Collect Data:
Unplug the micro:bit and connect the battery pack.
Place your micro:bit in the predetermined observation area.
Start data logging by pressing button A. Leave the micro:bit logging for a period of time.
Return to the micro:bit and press button B to stop logging.
Disconnect the battery pack and plug the micro:bit back into a computer.
Mild - Medium 🌶️🌶️ - Spicy
Pro Tip: Be sure to connect the micro:bit to a computer and save the MY_DATA file before pressing buttons A and B together to delete all data.

## Slide 24: Medium 🌶️🌶️ Student Activity Steps 4
Mild - Medium 🌶️🌶️ - Spicy
The MICROBIT drive will appear like a USB drive.
Look in the MICROBIT drive and open the MY_DATA file to see a table of your data in a web browser.
↓

## Slide 25: Medium 🌶️🌶️ Student Activity Steps 5
Mild - Medium 🌶️🌶️ - Spicy
Click the Visual preview button to see a graph of your data.
You can also click the Copy button and then paste your data into a spreadsheet.

## Slide 26: Medium 🌶️🌶️ Analyze Your Data 1
Mild - Medium 🌶️🌶️ - Spicy
Your data appears in a table in the web browser.
The time stamps in the log represent the amount of time that has passed since your micro:bit was powered on. If you log more than one set of data without clearing the log, you may not be able to see the visual preview of the data you want to study, so it’s a good idea to delete the previously stored log before starting a new experiment.

## Slide 27: Medium 🌶️🌶️ Analyze Your Data 2
Mild - Medium 🌶️🌶️ - Spicy
Click the Visual preview button above the data table to see a graph of your data:
The light and temperature data are logged and displayed within different number ranges. Click the labels to view a single data type in more detail with an appropriately scaled graph.
You can also click the Copy button and then paste your data into a spreadsheet.

## Slide 28: Medium 🌶️🌶️ Code Details 1
Mild - Medium 🌶️🌶️ - Spicy
When the program starts, the variable “logging” is set to false. An X icon is displayed to signal that data is not being logged. The data collection categories are organized in columns and named “temperature” and “light” for this project.
Pressing button A sets the variable “logging” to true and displays a checkmark to signal that data logging is happening. Pressing button B sets “logging” to false and displays an X to signal that data logging has ended.
This project uses a Boolean variable, which can only store one of two values - true or false. The Boolean variable is called “logging”, and it controls when the micro:bit logs data.

## Slide 29: Medium 🌶️🌶️ Code Details 2
Mild - Medium 🌶️🌶️ - Spicy
This program uses an infinite loop, the ‘every 60,000 ms’ block, that checks if the micro:bit is logging data every minute.
If the micro:bit is logging, it shows a heart on its LED display, records (logs) the temperature and light level data in the appropriate column, and then clears the display to signal that data logging is complete every minute.

## Slide 30: Medium 🌶️🌶️ Code Details 3
Mild - Medium 🌶️🌶️ - Spicy
The micro:bit's temperature sensor measures in Celsius.
The ‘convertCtoF function’ converts the temperature from Celsius to Fahrenheit by multiplying it by 1.8 and adding 32. Using a function to convert the temperature allows you to re-use the conversion code every time data is logged.
The function is used with the ‘call convertCtoF “temperature (℃)” ‘ block found within the infinite loop block of code.

## Slide 31: Medium 🌶️🌶️ Code Details 4
Mild - Medium 🌶️🌶️ - Spicy
Pressing buttons A + B together will delete all data in the log. The LED displays a skull icon to signal that data is erased, the ‘delete log’ block erases all data, and the data collection categories are assigned “temperature” and “light” so the micro:bit is ready to collect data the next time button A is pressed.
While unlikely, it is possible for the log to be full. When this happens, the variable “logging” is set to false and the full LED display lights up to signal that the log is full.

## Slide 32
Spicy

## Slide 33: Spicy 🌶️🌶️🌶️ Introduction 1
Mild - Medium - Spicy 🌶️🌶️🌶️
Students will download the code on their micro:bit, attach a battery pack, take it to the area they want to test, and start data logging.
Remember to identify the areas where students will be collecting data. Select areas with varying light and temperature levels to encourage interesting discussions.
Students will return to the area later to stop data logging and collect their micro:bits.
Students will connect their micro:bits to a computer or tablet to download the data collected. They can then view the data and graphs generated from their data logging on a webpage. They can also plot their own graphs from the data collected.

## Slide 34: Spicy 🌶️🌶️🌶️ Introduction 2
Mild - Medium - Spicy 🌶️🌶️🌶️
The micro:bit’s light sensor uses the display LEDs to measure light, so make sure the micro:bit’s LED display is pointing toward the light source. The light level reading will be a number between 0 (dark) and 255 (the most intense light the micro:bit can measure).
The temperature sensor is in the processor on the back of the micro:bit and provides a good approximation of the temperature around the device. It is important to remember that items touching the processor or
a person holding the micro:bit can impact the temperature reading, so students should not pick up the micro:bit to take readings. This project is programmed to display the temperature reading in Fahrenheit.

## Slide 35: Spicy 🌶️🌶️🌶️ Student Activity Steps 1
Build the code:
Open the environment data logger project: mbit.io/us-environment-spicy
Explain that students will use the toolbox to find code blocks. For this project, four parts of the code have already been done for them, and they control what happens when the program starts, when it is logging, when the log is full and converting the temperature from Celsius to Fahrenheit.
Explain that students will need to code three parts of the environment data logger:
  Code button A to start logging and show a checkmark icon.
  Code button B to stop logging and show an X icon.
  Code buttons A + B to delete the log, show a skull icon, and reset the data column headings to “temperature” and “light”.
Mild - Medium - Spicy 🌶️🌶️🌶️

## Slide 36: Spicy 🌶️🌶️🌶️ Student Activity Steps 2
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘on button A pressed’ block in the Input section and add it to your workspace.
Find the ‘set logging to’ block in the Variables section and add it into the ‘on button A pressed’ block.
Replace the 0 with a ‘true’ block from the Logic menu. Add a ‘show icon’ block with a checkmark underneath.
Build the code - button A:

## Slide 37: Spicy 🌶️🌶️🌶️ Student Activity Steps 3
Replace the 0 with a ‘false’ block from the Logic menu. Add a ‘show icon’ block with an X icon underneath.
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘on button A pressed’ block in the Input section and add it to your workspace. Click the down arrow and select B.
Find the ‘set logging to’ block in the Variables section and add it into the ‘on button B pressed’ block.
Build the code - button B:
↓

## Slide 38: Spicy 🌶️🌶️🌶️ Student Activity Steps 4
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘on button A pressed’ block in the Input section and add it to your workspace. Click the down arrow and select A + B.
Find the ‘show icon’ block in the Basic section. Add it, displaying a skull icon.
Add the ‘delete log’ and ‘set columns’ blocks from the Data Logger section. Add column headings “temperature” and “light”. Test the code using the simulator and then download the code to your micro:bit.
Build the code - buttons A + B:
↓

## Slide 39: Spicy 🌶️🌶️🌶️ Student Activity Steps 5
Unplug the micro:bit and connect the battery pack.
Place your micro:bit in the predetermined observation area.
Start data logging by pressing button A. Leave the micro:bit logging for a period of time.
Return to the micro:bit and press button B to stop logging.
Disconnect the battery pack and plug the micro:bit back into a computer.
Mild - Medium - Spicy 🌶️🌶️🌶️
Pro Tip: Be sure to connect the micro:bit to a computer and save the MY_DATA file before pressing buttons A and B together to delete all data.

## Slide 40: Spicy 🌶️🌶️🌶️ Student Activity Steps 6
Mild - Medium - Spicy 🌶️🌶️🌶️
The MICROBIT drive will appear like a USB drive.
Look in the MICROBIT drive and open the MY_DATA file to see a table of your data in a web browser.
↓

## Slide 41: Spicy 🌶️🌶️🌶️ Student Activity Steps 7
Mild - Medium - Spicy 🌶️🌶️🌶️
Click the Visual preview button to see a graph of your data.
You can also click the Copy button and then paste your data into a spreadsheet.

## Slide 42: Spicy 🌶️🌶️🌶️ Analyze Your Code 1
Mild - Medium - Spicy 🌶️🌶️🌶️
Your data appears in a table in the web browser.
The time stamps in the log represent the amount of time that has passed since your micro:bit was powered on. If you log more than one set of data without clearing the log, you may not be able to see the visual preview of the data you want to study, so it’s a good idea to delete the previously stored log before starting a new experiment.

## Slide 43: Spicy 🌶️🌶️🌶️ Analyze Your Code 2
Mild - Medium - Spicy 🌶️🌶️🌶️
Click the Visual preview button above the data table to see a graph of your data:
The light and temperature data are logged and displayed within different number ranges. Click the labels to view a single data type in more detail with an appropriately scaled graph.
You can also click the Copy button and then paste your data into a spreadsheet.

## Slide 44: Spicy 🌶️🌶️🌶️ Code Details 1
Mild - Medium - Spicy 🌶️🌶️🌶️
This project uses a Boolean variable, which can only store one of two values - true or false. The Boolean variable is called “logging” and it controls when the micro:bit logs data.
When the program starts, the variable “logging” is set to false. An X icon is displayed to signal that data is not being logged. The data collection categories are organized in columns and named “temperature” and “light” for this project.
Pressing button A sets the variable “logging” to true and displays a checkmark to signal that data logging is happening. Pressing button B sets “logging” to false and displays an X to signal that data logging has ended.

## Slide 45: Spicy 🌶️🌶️🌶️ Code Details 2
Mild - Medium - Spicy 🌶️🌶️🌶️
This program uses an infinite loop, the ‘every 60,000 ms’ block, that checks if the micro:bit is logging data every minute.
If the micro:bit is logging, it shows a heart on its LED display, records (logs) the temperature and light level data in the appropriate column, and then clears the display to signal that data logging is complete every minute.

## Slide 46: Spicy 🌶️🌶️🌶️ Code Details 3
Mild - Medium - Spicy 🌶️🌶️🌶️
The micro:bit's temperature sensor measures in Celsius.
The ‘convertCtoF function’ converts the temperature from Celsius to Fahrenheit by multiplying it by 1.8 and adding 32. Using a function to convert the temperature allows you to re-use the conversion code every time data is logged.
The function is used with the ‘call convertCtoF “temperature (℃)” ‘ block found within the infinite loop block of code.

## Slide 47: Spicy 🌶️🌶️🌶️ Code Details 4
Mild - Medium - Spicy 🌶️🌶️🌶️
Pressing buttons A + B together will delete all data in the log. The LED displays a skull icon to signal that data is erased, the ‘delete log’ block erases all data, and the data collection categories are assigned “temperature” and “light” so the micro:bit is ready to collect data the next time button A is pressed.
While unlikely, it is possible for the log to be full. When this happens, the variable “logging” is set to false and the full LED display lights up to signal that the log is full.

## Slide 48
Extension Ideas

## Slide 49: Environment Data Logger Extensions
Record data over a longer period of time, such as once an hour for several days.
Run the experiment in different places and compare your data.
Use data collected to design and engineer solutions to protect resources in your community.
Modify the code to study noise levels over time using the microphone.