## Slide 1: Lesson 4 Python step counter
Updated April 2026. Visit https://microbit.org/teach/ for most up-to-date resources.

## Slide 2: Recap: Python emotion badge
In Python we have to use an infinite while True: loop to keep checking if a button is pressed.
Notes: Recap that where MakeCode has ‘event blocks’ that respond to events like pressing a button, in Python we have to use an infinite loop keep checking if a button is pressed.

## Slide 3: Think: learning objectives
I can explain that the accelerometer is a sensor, an input that senses movement.
I can explain that variables are containers for storing data which can be accessed and updated.
I can write instructions in Python to turn my micro:bit into a step counter using the accelerometer and variables.

## Slide 4: Think: compare MakeCode to Python
Can you match instructions in MakeCode for a step counter with their equivalent in Python?
Notes: Recap that just as with the emotion badge, here we need an infinite while True: loop to keep checking if the accelerometer senses the micro:bit has been shaken. There is no ‘on shake’ event instruction in Python.

## Slide 5: Think: accelerometer
An accelerometer is an input that senses movement.
The step counter program uses the micro:bit’s accelerometer sensor to sense when your leg is moving.

## Slide 6: Think: variables and sequence
The code stores how many times the micro:bit has been shaken in a variable called steps.
Variables are containers for storing data, which can be accessed and updated while a program is running.
The sequence (order) of the instructions in the code is important. When the micro:bit is shaken, we must display the value of the steps variable, after increasing it by 1.

## Slide 7: Create: edit the code to make a step counter
Edit or replace the existing code carefully so it matches the code here. Lower case and capital letters are important!
If you delete the existing code in the Python Editor, leave from microbit import * at the top.
Use auto-complete or the reference to help you.
Be careful to indent the code correctly.
Test your program in the micro:bit simulator.

## Slide 8: Create: tweak the program – buttons
Tweak the program so that the number of steps you have taken only appears on the display if you press button A.
Get a button A is pressed snippet from the Reference in the Buttons section. Drag it under the existing code so that the if in lines 5 and 8 are lined up.
Replace the display.scroll('A') instruction with the display.show(steps) instruction.
Test out the program in the simulator.
Notes: Ask the students which program they prefer – the original or tweaked version – and why. Explain that the tweaked program would better conserve their batteries.

## Slide 9: Create: tweak the program – multiplication
Add an additional display.show(steps) instruction shown on line 7 so that you can see how many steps you have taken without pressing button A.
When wearing the step counter, you may find it only counts every other step. To fix this, modify the code (as shown on line 9) to multiply the steps variable by two when it’s displayed.
Notes: Students should alter line 9 so that it says display.show(steps * 2)

## Slide 10: Create: tweak the program – distance calculator
Measure the length of your average stride in metres and get your micro:bit to multiply this by the number of steps to calculate the distance you’ve walked after pressing button B.
Test your program in the simulator.
Notes: Other ideas: • When you take a step the step count shown is half that shown when you press button A. Can you fix this? (Make line 7 match line 9). • Do you think using display.scroll (which scrolls two digit numbers) is better than display.show (which shows one digit at a time)?

## Slide 11: Create: send to micro:bit
Send the code to your micro:bit using the purple Send to micro:bit button at the bottom of the screen. Follow the instructions on the screen.
Attach the micro:bit and battery pack to your leg or ankle.
You might like to try out the step counter outside.
Notes: Students transfer code to their micro:bits and test.
If you have battery packs, encourage students to unplug their micro:bits from computers and attach them.
Does it work as you expected? If not, do you need to debug the code and download it again?

## Slide 12: Extend Reward your efforts!
Can you adjust your step counter so that when you have done a certain number of steps, a happy emoji and encouraging message appears?
Go to the Reference then the Logic section and find the heading if, elif, else. Choose the if conditional statement snippet, add it to your program, and edit the code to show a reward.

## Slide 13: Evaluate
How does the step counter use the accelerometer sensor?
How does it use a variable?
How does coding in Python compare with block-based coding?
Did the project work as you expected?
How easy was it to modify and test the code?
What improvements did you make and why?
Notes: It uses the accelerometer motion sensor to sense when you take a step by using the ‘shake’ gesture.
It uses the steps variable to keep track of or store the current number of steps you have taken. The variable can then be updated by adding 1 to it every time the accelerometer senses it’s been shaken. The variable can also be accessed to display the current number of steps at any given time.

## Slide 14: Evaluate revisit the learning objectives
I can explain that the accelerometer is a sensor, an input that senses movement.
I can explain that variables are containers for storing data which can be accessed and updated.
I can write instructions in Python to turn my micro:bit into a step counter using the accelerometer and variables.

## Slide 15: Next steps
Today we learned about the accelerometer and variables to make a step counter.
Next time, we will learn about sensors and logic to make a nightlight.

## Slide 16: Visit microbit.org/teach for more lessons, projects, courses and help.
This content is published by the Micro:bit Educational Foundation under a Creative Commons Attribution-ShareAlike 4.0 International (CC BY-SA 4.0) licence