## Slide 1
Project guide
Including Audio Recordings with Funny Voice Recorder
Integrating CS with Literacy - 4th Grade
What you need:

## Slide 2: Including Audio Recordings with Funny Voice Recorder
Summary & Context
The BBC micro:bit has a built-in microphone and speaker. Students can use the micro:bit to add audio recordings, including their voice and sound effects, to support the main ideas or themes of a presentation.
micro:bit Feature:
Microphone Sensor
The micro:bit’s microphone can sense and record sounds, including your voice and noises. The microphone LED will light up to show when your micro:bit is recording sound. Use the micro:bit’s speaker to hear your recorded sounds.
Example: Use the micro:bit to record sounds that will be played to enhance presentations.

## Slide 3: Computer Science Concepts
Inputs
Inputs allow computers to sense things happening in the real world so they can act on them and make something happen.
This project uses the microphone sensor for input.
The microphone is on the back of the micro:bit V2, and on the front is a microphone LED next to the hole that lets the sound in. It lights up to show when your micro:bit is recording sounds.
Outputs
Outputs are data sent from a computer to communicate with the user, such as the information shown on the LED display.
This project uses the speaker for sound output.
The built-in speaker allows you to make expressive and useful projects.

## Slide 4: How the Funny Voice Recorder Works
Record your voice or a sound using the micro:bit’s microphone and play it back speeded up.
Press button A and speak into the microphone and button B to play back the recorded sound. It plays back twice as fast, making your voice speed up and sound squeaky!
The code sets the sample rate to 10,000 hertz (Hz) for recording. This means the micro:bit measures or samples sound from the microphone 10,000 times every second.
During playback, the samples will be played twice as quickly, 20,000 times every second. This doubles the pitch of any recorded sounds.
Adjust the playback rate to lower than 10,000 hertz to slow down sounds.
Pro tip: To delete a recording, record a new sound over it, press the reset button on the back of your micro:bit, or unplug the micro:bit from its power source (USB or battery pack).

## Slide 5: Pick Your Level
Mild 🌶️ 30 mins | Learning outcome: I can add audio recordings using the micro:bit funny voice recorder to develop the main idea or theme of a presentation.
 | Activity description: Using existing code, students will create audio recordings using a micro:bit to develop the main idea or theme of a presentation.
Medium 🌶️🌶️ 45 mins | Learning outcome: I can modify my own funny voice recorder program to develop the main idea or theme of a presentation.
 | Activity description: Modify the starter project to code your own funny voice recorder to develop the main idea or theme of a presentation using audio recordings.
Spicy 🌶️🌶️🌶️ 45-60 mins | Learning outcome: I can create my own funny voice recorder program to develop the main idea or theme of a presentation.
 | Activity description: Code your own funny voice recorder program to develop the main idea or theme of a presentation using audio recordings.

## Slide 6
Mild

## Slide 7: Mild 🌶️ Introduction
Students will download the code onto their micro:bit and use their micro:bit as a recorder and a speaker.
Press button A and speak into the microphone. A square appears on the LED display while it’s recording.
Press button B to play back the recorded sound. It plays back twice as fast, making your voice speed up and sound squeaky!
Students can record their voice or sound effects that will develop the main idea or theme of a presentation.
Mild 🌶️ - Medium - Spicy
Pro tip: To delete a recording, record a new sound over it, press the reset button on the back of your micro:bit, or unplug the micro:bit from its power source (USB or battery pack).
Notes: https://drive.google.com/file/d/1AwLdjKRa3QnwDeicf5kPsx20PO0fmaEz/view?usp=sharing

## Slide 8: Mild 🌶️ Student Activity Steps
Open the project: mbit.io/us-voice and download the code to the micro:bit.
Unplug the micro:bit and attach a battery pack.
Read through your presentation to decide which sounds you would like to add to enhance your presentation and when you will play those sounds.
Press button A and speak into the microphone.
Press button B to play back the speeded-up sounds. Does it sound like you hoped it would? If not, re-record your sounds.
Practice doing your presentation with your sound effects. When you are ready, try it in front of an audience.
Mild 🌶️ - Medium - Spicy
Pro tip: Be mindful of background noise when recording. Consider allowing students to use a quiet space to record such as the hallway or library.

## Slide 9: Mild 🌶️ Code Details 1
This project uses the microphone to record your sounds and the speaker to play them back at higher speed, producing a funny sound effect.
Mild 🌶️ - Medium - Spicy
When button A is pressed, the ‘set sample rate to 10,000 for recording’ block sets the sample rate to 10,000 hertz (Hz), meaning sound is sampled from the micro:bit 10,000 times per second for a maximum of three seconds. A small square is shown on the LED display while the microphone is recording. The LED screen is cleared to signal that the audio recording is done.

## Slide 10: Mild 🌶️ Code Details 2
Mild 🌶️ - Medium - Spicy
When button B is pressed, the ‘set sample rate to 20,000 for playback’ block sets the playback rate to 20,000 hertz (Hz), or 20,000 times per second. It plays back twice as fast and doubles the pitch of any sounds recorded. The LED screen is cleared to signal the end of the recording.

## Slide 11
Medium

## Slide 12: Medium 🌶️🌶️ Introduction
Students open a starter project containing all the blocks they need to make the project.
After the code has been built, students will download the code onto their micro:bit and use their micro:bit to record and play back sounds.
Press button A and speak into the microphone. A square appears on the LED display while it’s recording.
Press button B to play back the recorded sound. It plays back twice as fast, making your voice speed up and sound squeaky!
Students can record their voice or sound effects that will develop the main idea or theme of a presentation.
Mild - Medium 🌶️🌶️ - Spicy
Pro tip: To delete a recording, record a new sound over it, press the reset button on the back of your micro:bit, or unplug the micro:bit from its power source (USB or battery pack).

## Slide 13: Medium 🌶️🌶️ Student Activity Steps 1
Build the Code - On Button A Pressed:
Open the starter project: mbit.io/us-voice-pp
Explain that students have all the code blocks they need.
Explain that they will be building their own funny voice recorder.
Code button A to set the sample rate for recording to 10,000. Then show a small square icon to indicate that the micro:bit is recording, record an audio clip until done, then the screen is cleared.
Make sure student code looks like:
Mild - Medium 🌶️🌶️ - Spicy

## Slide 14: Medium 🌶️🌶️ Student Activity Steps 2
Build the Code - On Button B Pressed:
Code button B to set the sample rate for playback at 20,000, then show the symbol for ‘play’ to indicate that the micro:bit is playing the recording until done, then the screen is cleared.
Make sure student code looks like:
Mild - Medium 🌶️🌶️ - Spicy
Pro tip: ‘Until done’ plays an audio clip once, whereas ‘in background’ will play the sound file in a loop while other code instructions are read and carried out.

## Slide 15: Medium 🌶️🌶️ Student Activity Steps 3
Record and Play Back Sounds for a Presentation:
Download the code to the micro:bit.
Unplug the micro:bit and attach a battery pack.
Read through your presentation to decide which sounds you would like to add to enhance your presentation and when you will play those sounds.
Press button A and speak into the microphone.
Press button B to play back the speeded-up sounds. Does it sound like you hoped it would? If not, re-record your sounds.
Practice doing your presentation with your sound effects. When you are ready, try it in front of an audience.
Mild - Medium 🌶️🌶️ - Spicy
Pro tip: Be mindful of background noise when recording. Consider allowing students to use a quiet space to record such as the hallway or library.

## Slide 16: Medium 🌶️🌶️ Code Details 1
Mild - Medium 🌶️🌶️ - Spicy
This project uses the microphone to record your sounds and the speaker to play them back at higher speed, producing a funny sound effect.
When button A is pressed, the ‘set sample rate to 10,000 for recording’ block sets the sample rate to 10,000 hertz (Hz), meaning sound is sampled from the micro:bit 10,000 times per second for a maximum of three seconds. A small square is shown on the LED display while the microphone is recording. The LED screen is cleared to signal that the audio recording is done.

## Slide 17: Medium 🌶️🌶️ Code Details 2
Mild - Medium 🌶️🌶️ - Spicy
When button B is pressed, the ‘set sample rate to 20,000 for playback’ block sets the playback rate to 20,000 hertz (Hz), or 20,000 times per second. It plays back twice as fast and doubles the pitch of any sounds recorded. The LED screen is cleared to signal the end of the recording.

## Slide 18
Spicy

## Slide 19: Spicy 🌶️🌶️🌶️ Introduction
Students open Microsoft MakeCode and code their funny voice recorder.
After the code has been built, students will download the code on their micro:bit and use their micro:bit as a recorder and a speaker.
Press button A and speak into the microphone. A square appears on the LED display while it’s recording.
Press button B to play back the recorded sound. It plays back twice as fast, making your voice speed up and sound squeaky!
Students can record their voice or sound effects that will develop the main idea or theme of a presentation.
Mild - Medium - Spicy 🌶️🌶️🌶️
Pro tip: To delete a recording, record a new sound over it, press the reset button on the back of your micro:bit, or unplug the micro:bit from its power source (USB or battery pack).

## Slide 20: Spicy 🌶️🌶️🌶️ Student Activity Steps 1
Mild - Medium - Spicy 🌶️🌶️🌶️
Build the Code:
Open Microsoft MakeCode: microbit.makecode.org
Explain that students will use the toolbox to find code blocks.
Click on Extensions in the menu, then audio-recording to install the Record section of the MakeCode editor.
Delete the ‘on start’ and ‘forever’ blocks by dragging and dropping them onto the menu. You won’t need these blocks in this project.

## Slide 21: Spicy 🌶️🌶️🌶️ Student Activity Steps 2
Find the ‘set sample rate to’ block from the Record menu and put it inside the ‘on button A pressed’ block.
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘on button A pressed’ block in the Input section and add it to your workspace.
Build the Code - On Button A Pressed part 1:
Change the sample rate from 11,000 to 10,000. Click the plus button and choose ‘recording’ from the drop-down options.

## Slide 22: Spicy 🌶️🌶️🌶️ Student Activity Steps 3
Add the ‘record audio clip until done’ block from the Record menu.
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘show icon’ block in the Basic section. Put the block under the ‘set sample rate’ block and select the arrow to select the built-in small square image.
Build the Code - On Button A Pressed part 2:

## Slide 23: Spicy 🌶️🌶️🌶️ Student Activity Steps 4
Add a ‘clear screen’ block from the Basic menu.
Mild - Medium - Spicy 🌶️🌶️🌶️
Build the Code - On Button A Pressed part 3:

## Slide 24: Spicy 🌶️🌶️🌶️ Student Activity Steps 5
Mild - Medium - Spicy 🌶️🌶️🌶️
Drag an ‘on button A pressed’ block into the workspace and use the drop-down arrow to change the A to a B.
Find a ‘set sample rate to’ block in the Record menu. Add it to the ‘on button B pressed’ block and change the 11,000 to 20,000. Click on the plus button and select ‘for playback’ from the drop-down options.
Build the Code - On Button B Pressed part 1:
↓

## Slide 25: Spicy 🌶️🌶️🌶️ Student Activity Steps 6
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘play audio clip until done’ block in the Record section and put it underneath the play icon.
Build the Code - On Button B Pressed part 2:
Find the ‘show leds’ block from the Basic section and click on the individual LEDs to make a ‘play’ icon.

## Slide 26: Spicy 🌶️🌶️🌶️ Student Activity Steps 7
Add the ‘clear screen’ block from the Basic menu.
Mild - Medium - Spicy 🌶️🌶️🌶️
Build the Code - On Button B Pressed part 3:

## Slide 27: Spicy 🌶️🌶️🌶️ Student Activity Steps 8
Download the code to the micro:bit.
Unplug the micro:bit and attach a battery pack.
Read through your presentation to decide which sounds you would like to add to enhance your presentation and when you will play those sounds.
Press button A and speak into the microphone.
Press button B to play back the speeded-up sounds. Does it sound like you hoped it would? If not, re-record your sounds.
Practice doing your presentation with your sound effects. When you are ready, try it in front of an audience.
Mild - Medium - Spicy 🌶️🌶️🌶️
Pro tip: Be mindful of background noise when recording. Consider allowing students to use a quiet space to record such as the hallway or library.

## Slide 28: Spicy 🌶️🌶️🌶️ Code Details 1
Mild - Medium - Spicy 🌶️🌶️🌶️
This project uses the microphone to record your sounds and the speaker to play them back at higher speed, producing a funny sound effect.
When button A is pressed, the ‘set sample rate to 10,000 for recording’ block sets the sample rate to 10,000 hertz (Hz), meaning sound is sampled from the micro:bit 10,000 times per second for a maximum of three seconds. A small square is shown on the LED display while the microphone is recording. The LED screen is cleared to signal that the audio recording is done.

## Slide 29: Spicy 🌶️🌶️🌶️ Code Details 2
Mild - Medium - Spicy 🌶️🌶️🌶️
When button B is pressed, the ‘set sample rate to 20,000 for playback’ block sets the playback rate to 20,000 hertz (Hz), or 20,000 times per second. It plays back twice as fast and doubles the pitch of any sounds recorded. The LED screen is cleared to signal the end of the recording.

## Slide 30
Extension Ideas

## Slide 31: Funny Voice Recorder Extensions
Further address standard SL.4.5: Add audio recordings and visual displays to presentations when appropriate to enhance the development of main ideas or themes.
  Add visual images and animations to accompany the sounds.
Instead of speeding up your voice or a sound, try slowing it down. When might you use this? Why?
Use other inputs such as button A plus B to add music to enhance your performance.