## Slide 1: What you need:
Project guide
Magnetic Force with Simple Door Alarm
Integrating CS with Science - 3rd Grade
What you need:
Magnet
Adhesive putty

## Slide 2: Simple Door Alarm
Summary & Context
The BBC micro:bit has a built-in magnetometer that can detect magnetic fields. Students can use the micro:bit to observe that magnets can interact with objects like the micro:bit without touching them to develop understanding of magnetic fields.
Students can use the magnetometer and a magnet to make a simple door alarm. Then students can extend their learning by using the micro:bit to design and create solutions to their own problems such as an alarm for their desk or locker.
This activity requires a magnet.
micro:bit Feature: Magnetometer
The compass can also be used to measure the strength of the Earth's magnetic field and other magnetic fields. In MakeCode it measures magnetic field strength in microTeslas.

## Slide 3: Computer Science Concepts
Forever Loops
Loops tell the computer to do an instruction (or set of instructions) over and over again. There are different types of loops including infinite, count-controlled, and condition-controlled loops.
This program uses a forever loop (infinite loop), which means the computer repeats the same steps endlessly. In this project, it is constantly checking for a circuit.
Selection/Conditionals
Conditionals tell the computer to perform an instruction (or set of instructions) only when certain conditions are met. If-then-else statements are a very common type of conditional.
Classrooms are full of if-then-else conditions:
If it rains, then we have indoor recess or else we will have outdoor recess.
Notes: Used m:b, CSTA, and Code.org glossaries to build content

## Slide 4: How the Simple Door Alarm Works
A magnet is attached on the corner of a door, and the micro:bit is attached close to it on the door frame.
The program uses the magnetometer’s input sensor and a forever loop to continue measuring the strength of the magnetic field.
The program uses selection so that when the strength of the magnetic field falls below a certain level (the threshold), an angry face shows on the LED display.
This means when the door was opened, the magnet moved away from the micro:bit, signaling that someone may have been in your room.
Pro tip: Make sure the magnet and micro:bit are close together when the door is closed.

## Slide 5: Pick Your Level
Mild 🌶️ 30 mins | Learning outcome: I can observe and ask questions about magnetic fields using the micro:bit simple door alarm.
 | Activity description: Using existing code, build a simple door alarm using a micro:bit and a magnet to model how magnetic fields interact without objects touching each other.
Medium 🌶️🌶️ 45 mins | Learning outcome: I can modify my own simple door alarm program to observe and ask questions about magnetic fields.
 | Activity description: Modify the starter project to code your own simple door alarm.
Spicy 🌶️🌶️🌶️ 45-60 mins | Learning outcome: I can create my own simple door alarm program to observe and ask questions about magnetic fields.
 | Activity description: Code your own simple door alarm program to observe and ask questions about magnetic fields.

## Slide 6
Mild

## Slide 7: Mild 🌶️ Introduction
Students will download the code on their micro:bit, and use with a magnet to explore magnetic fields and build a simple door alarm.
Attach a magnet in the corner of a door and attach the micro:bit near it on the door frame.
Students will test the alarm by opening and closing the door.
Because magnets have different magnetic field strengths, you and your students will take readings and adjust code as needed to improve the door alarm.
If it is not possible to make a door alarm, you can do the same experiment with a box.
Mild 🌶️ - Medium - Spicy

## Slide 8: Mild 🌶️ Student Activity Steps 1
Open the project: mbit.io/us-door and download the code to the micro:bit.
Unplug the micro:bit and connect the battery pack.
Attach a magnet to the corner of a door with adhesive putty.
Attach a micro:bit close to it on the door frame.
Observe what happens when the door is opened and closed. Is the alarm triggered when the door is opened? How well do you think it works?
Press button B if you need to reset the alarm.
Review knowledge of magnetic field strength, specifically that some magnets are stronger than others. This means the universal threshold number in this project may not work for all magnets.
Mild 🌶️ - Medium - Spicy

## Slide 9: Mild 🌶️ Student Activity Steps 2
Record the magnetic force reading with the door open and closed by pressing button A and noting the numbers on the micro:bit LED display.
Choose a new value to test by picking a number midway between your closed door and open door readings.
Adjust your code by replacing your new reading in second part of the “magnetic force strength” comparison block (see example).
Download your new code and test it.
Observe whether the door alarm works better or worse than before. How does your knowledge of magnetic field strength support your conclusion?
Mild 🌶️ - Medium - Spicy

## Slide 10: Mild 🌶️ Code Details 1
This project uses the micro:bit’s magnetometer to measure the strength of a magnetic field.
Mild 🌶️ - Medium - Spicy
The project uses a forever loop, meaning it is continuously checking the strength of the magnetic field.
It uses selection/conditionals to check if a condition has been met - specifically if the magnetic field strength is under the threshold identified (e.g. 200 in the code above).
If the magnetic field strength is under the threshold, an angry face will appear on the micro:bit’s LED display. This indicates the door has been opened.

## Slide 11: Mild 🌶️ Code Details 2
The project also allows you to show the magnetic force strength reading by pressing button A. This is useful when you need to make adjustments to the threshold.
Pressing button B clears the angry face and resets the alarm. A checkmark is displayed to confirm the alarm is reset.
Mild 🌶️ - Medium - Spicy

## Slide 12
Medium

## Slide 13: Medium 🌶️🌶️ Introduction
Students open the starter project containing all the blocks they need to make the project.
After the code has been built and downloaded onto their micro:bit, students will use it with a magnet to explore magnetic fields and build a simple door alarm.
Attach a magnet in the corner of a door and attach the micro:bit near it on the door frame.
Students will test the alarm by opening and closing the door.
Because magnets have different magnetic field strengths, you and your students will take readings and adjust code as needed to improve the door alarm.
If it is not possible to make a door alarm, you can do the same experiment with a box.
Mild - Medium 🌶️🌶️ - Spicy

## Slide 14: Medium 🌶️🌶️ Student Activity Steps 1
Build the code:
Open the starter project: mbit.io/us-door-pp
Explain that students have all the code blocks they need.
Explain that they will be building their own simple door alarm.
Use the ‘on button A pressed’ block to show the magnetic force strength reading.
Make sure student code looks like:
Mild - Medium 🌶️🌶️ - Spicy

## Slide 15: Medium 🌶️🌶️ Student Activity Steps 2
Use the ‘forever’ block to continuously test the magnetic force strength.
Explain that if the magnetic force strength reading is under the threshold, an angry face icon will appear on the micro:bit’s LED display.
Make sure student code looks like:
Code button B to clear the display and then show a checkmark icon when pressed.
Make sure student code looks like:
Test their code using the simulator.
Download the code to their micro:bit.
Mild - Medium 🌶️🌶️ - Spicy

## Slide 16: Medium 🌶️🌶️ Student Activity Steps 3
Try out your simple door alarm:
Unplug the micro:bit and connect the battery pack.
Attach a magnet to the corner of a door with adhesive putty.
Attach a micro:bit close to it on the door frame.
Observe what happens when the door is opened and closed. Is the alarm triggered when the door is opened? How well do you think it works?
Press button B if you need to reset the alarm.
Review knowledge of magnetic field strength, specifically that some magnets are stronger than others. This means the universal threshold number in this project may not work for all magnets.
Mild - Medium 🌶️🌶️ - Spicy

## Slide 17: Medium 🌶️🌶️ Student Activity Steps 4
Record the magnetic force reading with the door open and closed by pressing button A and noting the numbers on the micro:bit’s LED display.
Calculate a new value to test by picking a number midway between your closed door and open door readings.
Adjust your code by replacing your new reading in second part of the “magnetic force strength” comparison block (see example).
Download your new code and test it.
Observe whether the door alarm works better or worse than before. How does your knowledge of magnetic field strength support your conclusion?
Mild 🌶️ - Medium - Spicy

## Slide 18: Medium 🌶️🌶️ Code Details 1
This project uses the micro:bit’s magnetometer to measure the strength of a magnetic field.
Mild - Medium 🌶️🌶️ - Spicy
The project uses a forever loop, meaning it is continuously checking the strength of the magnetic field.
It uses selection/conditionals to check if a condition has been met - specifically if the magnetic field strength is under the threshold identified (e.g. 200 in the code above).
If the magnetic field strength is under the threshold, an angry face will appear on the micro:bit’s LED display. This indicates the door has been opened.

## Slide 19: Medium 🌶️🌶️ Code Details 2
Mild - Medium 🌶️🌶️ - Spicy
The project also allows you to show the magnetic force strength reading by pressing button A. This is useful when you need to make adjustments to the threshold.
Pressing button B clears the angry face and resets the alarm. A checkmark is displayed to confirm the alarm is reset.

## Slide 20
Spicy

## Slide 21: Spicy 🌶️🌶️🌶️ Introduction
Students open Microsoft MakeCode and code their own simple door alarm.
After the code has been built and downloaded onto their micro:bit, students will use it with a magnet to explore magnetic fields and build a simple door alarm.
Attach a magnet in the corner of a door and attach the micro:bit near it on the door frame.
Students will test the alarm by opening and closing the door.
Because magnets have different magnetic field strengths, you and your students will take readings and adjust code as needed to improve the door alarm.
If it is not possible to make a door alarm, you can do the same experiment with a box.
Mild - Medium - Spicy 🌶️🌶️🌶️

## Slide 22: Spicy 🌶️🌶️🌶️ Student Activity Steps 1
Build the code:
Open Microsoft MakeCode: microbit.makecode.org
Explain that students will use the toolbox to find code blocks.
Explain that they will be building their own simple door alarm.
Mild - Medium - Spicy 🌶️🌶️🌶️

## Slide 23: Spicy 🌶️🌶️🌶️ Student Activity Steps 2
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘on button A pressed’ block in the Input section and add it to your workspace.
Find the ‘show number’ block in the Basic section. Put it inside the ‘on button A pressed’ block.
Find the magnetic force block in the Input section by clicking on ‘more…’ Drop it over the 0 on the ‘show number’ block to replace it. Magnetic force can be measured in three directions - x, y, and z - or as an overall ‘strength’. Use the drop-down arrow to select ‘strength’. You will see the magnetic force strength reading when button A is pressed.
Build the code - button A:

## Slide 24: Spicy 🌶️🌶️🌶️ Student Activity Steps 3
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘forever’ block in the Basic section and add it to your workspace. The ‘forever’ block creates an infinite loop.
Find an ‘if true then’ block from the Logic section. Put it inside the ‘forever’ block.
An ‘if true then’ block is used to include conditionals in your program.
Find the ‘less than comparison’ block in the Logic section. Drop the comparison block over ‘true’ in the ‘if true then’ block. This will allow you to compare the values of the magnetic strength reading and the threshold used.
Build the code - forever part 1:

## Slide 25: Spicy 🌶️🌶️🌶️ Student Activity Steps 4
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the magnetic force block in the Input section by clicking on ‘more…’ Drop it over the first 0 on the ‘less than comparison’ block to replace it. Use the drop-down arrow to select ‘strength’. Type the threshold number, initially 200, over the second 0.
Find the ‘show icon’ block and put it under ‘if magnetic force strength < 200’. Use the drop-down to display an angry face.
Build the code - forever part 2:

## Slide 26: Spicy 🌶️🌶️🌶️ Student Activity Steps 5
Mild - Medium - Spicy 🌶️🌶️🌶️
Build the code - button B:
Drag the ‘on button A pressed’ block into the workspace from the Input section and use the drop-down menu to change the A to a B.
Put the ‘show icon’ block from the Basic category under the ‘clear screen’ block and use the drop-down arrow to find the checkmark icon.
Add a ‘clear screen’ block from the Basic category inside the ‘on button B pressed’ block.
↓

## Slide 27: Spicy 🌶️🌶️🌶️ Student Activity Steps 6
Try out your simple door alarm:
Unplug the micro:bit and connect the battery pack.
Attach a magnet to the corner of a door with adhesive putty.
Attach a micro:bit close to it on the door frame.
Observe what happens when the door is opened and closed. Is the alarm triggered when the door is opened? How well do you think it works?
Press button B if you need to reset the alarm.
Review knowledge of magnetic field strength, specifically that some magnets are stronger than others. This means the universal threshold number in this project may not work for all magnets.
Mild - Medium - Spicy 🌶️🌶️🌶️

## Slide 28: Spicy 🌶️🌶️🌶️ Student Activity Steps 7
Record the magnetic force reading with the door open and closed by pressing button A and noting the numbers on the micro:bit’s LED display.
Calculate a new value to test by picking a number midway between your closed door and open door readings.
Adjust your code by replacing your new reading in second part of the “magnetic force strength” comparison block (see example).
Download your new code and test it.
Observe whether the door alarm works better or worse than before. How does your knowledge of magnetic field strength support your conclusion?
Mild 🌶️ - Medium - Spicy

## Slide 29: Spicy 🌶️🌶️🌶️ Code Details 1
Mild - Medium - Spicy 🌶️🌶️🌶️
The project uses a forever loop, meaning it is continuously checking the strength of the magnetic field.
It uses selection/conditionals to check if a condition has been met - specifically if the magnetic field strength is under the threshold identified (e.g. 200 in the code above).
If the magnetic field strength is under the threshold, an angry face will appear on the micro:bit’s LED display. This indicates the door has been opened.
This project uses the micro:bit’s magnetometer to measure the strength of a magnetic field.

## Slide 30: Spicy 🌶️🌶️🌶️ Code Details 2
Mild - Medium - Spicy 🌶️🌶️🌶️
The project also allows you to show the magnetic force strength reading by pressing button A. This is useful when you need to make adjustments to the threshold.
Pressing button B clears the angry face and resets the alarm. A checkmark is displayed to confirm the alarm is reset.

## Slide 31
Extension Ideas

## Slide 32: Simple Door Alarm Extensions
Where else might you use an alarm? Adapt the simple alarm to protect your desk, locker, or backpack.
Add a speaker and an audible alarm.
Use a variable to count the number of times your door has been opened - you’ll need to add code to sense when it’s been opened and closed.
Create a timer to measure how long a door has been left open.