## Slide 1: What you need:
Project guide
Paraphrasing Quantitative Information with Survey Data Logger
Integrating CS with Literacy - 4th Grade
Outdoor space

## Slide 2: Paraphrasing Quantitative Information with Traffic Survey Data Logger
micro:bit Feature: Buttons
Buttons are a very common input device. The micro:bit has two buttons that can be programmed – buttons A and B.
Example: Students can observe different vehicles used to travel to school, including cars, buses, and trucks/vans. They can record their count for each using the micro:bit’s buttons.
Summary & Context
Students will use the BBC micro:bit as a data logger to collect observation data from their environment. For example, they might log data related to different modes of transportation to school or litter on the school grounds. They will connect the micro:bit to a computer and then paraphrase the visual preview of data collected.
This activity may require an additional 45-60 minutes to fully engage students in creating the data logger and in collecting and analyzing survey data.

## Slide 3: Computer Science Concepts
Inputs
Inputs allow computers to sense things happening in the real world so they can act on them and make something happen.
This project uses multiple buttons and the touch sensor for input:
Press button A to record when you see a car.
Press button B to record when you see a bus.
Press the touch logo when you see a truck or van.
Press buttons A + B to delete any old data stored on the micro:bit.

## Slide 4: How the Traffic Survey Data Logger Works
At the press of a button, the micro:bit records what you have seen and stores the data in a table so you can analyze it later.
Press button A when you see a car, button B when you see a bus, and the gold touch logo when you see a truck or van.
You can record data anywhere if you unplug the micro:bit from your computer and connect a battery pack.
Data stays on your micro:bit even if you disconnect the batteries, so you can study it when you’re back at your computer.
After you’ve collected your data, plug the micro:bit into a computer to see a table of all the traffic you recorded in a web browser.
Pro tip: Make sure you hold your micro:bit by the edges so you don’t record any data by accident.

## Slide 5: Pick Your Level
Mild 🌶️ 30 mins | Learning outcome: I can paraphrase quantitative data collected using the micro:bit traffic survey data logger.
 | Activity description: Using existing code, collect observational data and paraphrase the visual preview of data logged using the micro:bit traffic survey data logger.
Medium 🌶️🌶️ 45 mins | Learning outcome: I can modify my own micro:bit traffic survey data logger program to collect and paraphrase quantitative data.
 | Activity description: Modify the starter project to code your own traffic survey data logger program to collect observational data and paraphrase the visual preview of data logged.
Spicy 🌶️🌶️🌶️ 45-60 mins | Learning outcome: I can create my own micro:bit traffic survey data logger program to collect and paraphrase quantitative data.
 | Activity description: Code your own traffic survey data logger program to collect observational data and paraphrase the visual preview of data logged.

## Slide 6
Mild

## Slide 7: Mild 🌶️ Introduction
Students will download the code onto their micro:bit, take it outside (connected to the battery pack), and gather real-world data. This activity may require an additional 45-60 minutes to fully engage students in creating the data logger and in collecting and analyzing survey data.
Counting moving vehicles is hard, so working in pairs or small groups can be helpful.
This project is set up to measure cars with button A, buses with button B, and trucks or vans by pressing the touch logo, but you can tailor inputs to best suit your class and environment. You can rename the column headings, for example, to customize your use of this project. (Instructions are available at the end of this guide.)
Remember to identify the areas where students will be collecting data. A selection of areas can provide interesting discussions at the end of the session.
Students will connect their micro:bits to a computer or tablet to view the data and graphs generated from their data logging on a web page and paraphrase it. They can also analyze their data by creating their own graphs using paper and pencil or a spreadsheet.
Mild 🌶️ - Medium - Spicy

## Slide 8: Mild 🌶️ Student Activity Steps 1
Open the project: mbit.io/us-traffic-survey and download the code to the micro:bit.
Unplug the micro:bit and connect the battery pack.
Go to the predetermined observation area and start collecting data.
Collect data using the buttons to increase each count by 1. (Button A = cars, button B = buses, touch logo = trucks or vans.)
Mild 🌶️ - Medium - Spicy
Pro tip: Students can press buttons A and B together to delete the log and start the survey again.

## Slide 9: Mild 🌶️ Student Activity Steps 2
Disconnect the battery pack and plug the micro:bit back into a computer.
The MICROBIT drive will appear like a USB drive.
Look in the MICROBIT drive and open the MY_DATA file to see a table of your data in a web browser.
The times recorded in the table show the amount of time that passed since your micro:bit was powered on.
Paraphrase the data you have gathered.
Mild 🌶️ - Medium - Spicy
↓

## Slide 10: Mild 🌶️ Analyze Your Data 1
Mild 🌶️ - Medium - Spicy
Students will paraphrase the traffic survey data collected using the data table that appears in a web browser.
Students can analyze their data using paper and pencil or a spreadsheet.
Use paper and pencil to add up the total of each column to make your own column or bar chart to visualize your survey data.

## Slide 11: Mild 🌶️ Analyze Your Data 2
Mild 🌶️ - Medium - Spicy
To use a spreadsheet, you can:
Press the copy button to copy the data so you can paste it straight into a spreadsheet.
Press the download button to download the data as a CSV (comma separated values) file, which you can also import into a spreadsheet.

## Slide 12: Mild 🌶️ Code Details 1
This project uses the micro:bit’s data logging feature to record the number of cars, buses, and trucks.
Mild 🌶️ - Medium - Spicy
When the program starts, the data logging table’s column headings are set as “car”, “bus”, and “truck”. A ‘yes’ icon appears on the LED display.
When you press button A, a ‘show leds’ block is used to display a symbol for a car and a ‘1’ is logged in the “car” column of your data table. The LED display is then cleared.

## Slide 13: Mild 🌶️ Code Details 2
Mild 🌶️ - Medium - Spicy
When you press button B, a ‘show leds’ block is used to display a symbol for a bus and a ‘1’ is logged in the “bus” column of your data table. The LED display is then cleared.
When you press the micro:bit’s touch logo, a ‘show leds’ block is used to display a symbol for a truck and a ‘1’ is logged in the “truck” column of your data table. The LED display is then cleared.

## Slide 14: Mild 🌶️ Code Details 3
Mild 🌶️ - Medium - Spicy
When you press buttons A and B at the same time, a skull icon appears on the micro:bit’s LED display, the log is cleared of data, and the data logging table’s column headings are reset. Then a ‘yes’ icon appears on the LED display to indicate that the micro:bit is ready to collect new data.

## Slide 15
Medium

## Slide 16: Medium 🌶️🌶️ Introduction
Students open a starter project containing all the blocks they need to make the project. Some code has already been built. Students need to use the remaining blocks to finish their traffic survey data logger. This activity may require an additional 45-60 minutes to fully engage students in creating the data logger and in collecting and analyzing survey data.
Counting moving vehicles is hard, so working in pairs or small groups can be helpful.
This project is set up to measure cars with button A, buses with button B, and trucks or vans by pressing the touch logo, but you can tailor inputs to best suit your class and environment. You can rename the column headings to customize your use of this project. (Instructions are available at the end of this guide.)
Remember to identify the areas where students will be collecting data. A selection of areas can provide interesting discussions at the end of the session.
Students will connect their micro:bits to a computer or tablet to view the data and graphs generated from their data logging on a web page and paraphrase it. They can also analyze their data by creating their own graphs using paper and pencil or a spreadsheet.
Mild - Medium 🌶️🌶️ - Spicy

## Slide 17: Medium 🌶️🌶️ Student Activity Steps 1
Build the code - Part 1:
Open the starter project: mbit.io/us-traffic-survey-pp
Explain that students have all the code blocks they need. For this project, one part of the code is already done for them. This piece of code ensures that when the program starts, the data logging table’s column headings are set as “car”, “bus”, and “truck”, and then a ‘yes’ icon appears on the LED display.
Code button A to show a car icon on the micro:bit’s display and add a ‘1’ to the car column in the data logging table. Then clear the screen.
Make sure student code looks like:
Mild - Medium 🌶️🌶️ - Spicy

## Slide 18: Medium 🌶️🌶️ Student Activity Steps 2
Build the code - Part 2:
Code button B to show a bus icon on the micro:bit’s LED display and add a ‘1’ to the bus column in the data logging table. Then clear the screen.
Code the touch logo to show a truck icon on the LED display and add a ‘1’ to the truck column in the data logging table. Then clear the screen.
Make sure student code looks like:
Mild - Medium 🌶️🌶️ - Spicy

## Slide 19: Medium 🌶️🌶️ Student Activity Steps 3
Build the code - Part 3:
Build the blocks to show a skull icon on the LED display, delete the micro:bit’s data log, reset the column headings back to “car”, “bus”, and “truck”, then show a ‘yes’ icon when you press buttons A and B together.
Make sure student code looks like:
Test their code using the simulator and then download the code to their micro:bit.
Mild - Medium 🌶️🌶️ - Spicy

## Slide 20: Medium 🌶️🌶️ Student Activity Steps 4
Use your micro:bit to collect data:
Unplug the micro:bit and connect the battery pack.
Go to the predetermined observation area and start collecting data.
Collect data using the buttons to increase each count by 1. (Button A = cars, button B = buses, touch logo = trucks or vans.)
Mild - Medium 🌶️🌶️ - Spicy
Pro tip: Students can press buttons A and B together to delete the log and start the survey again.

## Slide 21: Medium 🌶️🌶️ Student Activity Steps 5
Mild - Medium 🌶️🌶️ - Spicy
Disconnect the battery pack and plug the micro:bit back into a computer.
The MICROBIT drive will appear like a USB drive.
Look in the MICROBIT drive and open the MY_DATA file to see a table of your data in a web browser.
The times recorded in the table show the amount of time that passed since your micro:bit was powered on.
Paraphrase the data you have gathered.
↓

## Slide 22: Medium 🌶️🌶️ Analyze Your Data 1
Mild - Medium 🌶️🌶️ - Spicy
Students will paraphrase the traffic survey data collected using the data table that appears in a web browser.
Students can analyze their data using paper and pencil or a spreadsheet.
Use paper and pencil to add up the total of each column to make your own column or bar chart to visualize your survey data.

## Slide 23: Medium 🌶️🌶️ Analyze Your Data 2
Mild - Medium 🌶️🌶️ - Spicy
To use a spreadsheet, you can:
Press the copy button to copy the data so you can paste it straight into a spreadsheet.
Press the download button to download the data as a CSV (comma separated values) file, which you can also import into a spreadsheet.

## Slide 24: Medium 🌶️🌶️ Code Details 1
Mild - Medium 🌶️🌶️ - Spicy
This project uses the micro:bit’s data logging feature to record the number of cars, buses, and trucks.
When the program starts, the data logging table’s column headings are set as “car”, “bus”, and “truck”. A ‘yes’ icon appears on the LED display.
When you press button A, a ‘show leds’ block is used to display a symbol for a car and a ‘1’ is logged in the “car” column of your data table. The LED display is then cleared.

## Slide 25: Medium 🌶️🌶️ Code Details 2
Mild - Medium 🌶️🌶️ - Spicy
When you press button B, a ‘show leds’ block is used to display a symbol for a bus and a ‘1’ is logged in the “bus” column of your data table. The LED display is then cleared.
When you press the micro:bit’s touch logo, a ‘show leds’ block is used to display a symbol for a truck and a ‘1’ is logged in the “truck” column of your data table. The LED display is then cleared.

## Slide 26: Medium 🌶️🌶️ Code Details 3
Mild - Medium 🌶️🌶️ - Spicy
When you press buttons A and B at the same time, a skull icon appears on the micro:bit’s LED display, the log is cleared of data, and the data logging table’s column headings are reset. Then a ‘yes’ icon appears on the LED display to indicate that the micro:bit is ready to collect new data.

## Slide 27
Spicy

## Slide 28: Spicy 🌶️🌶️🌶️ Introduction
Students open the traffic survey data logger project containing some pre-built code. Students will finish building their own traffic survey data logger using MakeCode. This activity may require an additional 45-60 minutes to fully engage students in creating the data logger and in collecting and analyzing survey data.
Counting moving vehicles is hard, so working in pairs or small groups can be helpful.
This project is set up to measure cars with button A, buses with button B, and trucks or vans by pressing the touch logo, but you can tailor inputs to best suit your class and environment. You can rename the column headings to customize your use of this project. (Instructions available at the end of this guide.)
Remember to identify the areas where students will be collecting data. A selection of areas can provide interesting discussions at the end of the session.
Students will connect their micro:bits to a computer or tablet to view the data and graphs generated from their data logging on a web page and paraphrase it. They can also analyze their data by creating their own graphs using paper and pencil or a spreadsheet.
Mild - Medium - Spicy 🌶️🌶️🌶️

## Slide 29: Spicy 🌶️🌶️🌶️ Student Activity Steps 1
Build the Code:
Open the traffic survey data logger project: mbit.io/us-traffic-survey-spicy
Explain that students will use the toolbox to find code blocks. For this project, two parts of the code are already done for them. They control what happens when the program starts and when the data log is deleted, including setting the data logging table column headings as “car”, “bus”, and “truck”.
Explain that students will need to code three parts of the traffic survey data logger:
  Code the micro:bit so that when you press button A, a car icon appears on the LED display and a ‘1’ is added to the car column of the data logging table.
  Code the micro:bit so that when you press button B, a bus icon appears on the LED display and a ‘1’ is added to the bus column of the data logging table.
  Code the micro:bit so that when you press the touch logo, a truck icon appears on the LED display and a ‘1’ is added to the truck column of the data logging table.
Mild - Medium - Spicy 🌶️🌶️🌶️

## Slide 30: Spicy 🌶️🌶️🌶️ Student Activity Steps 2
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘on button A pressed’ block in the Input section and add it to your workspace.
Find the ‘show leds’ block in the Basic section, add it to the ‘on button A pressed’ block, and select LEDs to draw a car symbol.
Build the code - button A part 1:

## Slide 31: Spicy 🌶️🌶️🌶️ Student Activity Steps 3
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘log data’ block and add it underneath. Add “car” into the column circle and ‘1’ into the value circle. This will mean a 1 is added into the “car” column when you press the button.
Build the code - button A part 2:
Find the ‘clear screen’ block in the Basic section and put it underneath.

## Slide 32: Spicy 🌶️🌶️🌶️ Student Activity Steps 4
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘on button A pressed’ block in the Input section and add it to your workspace. Use the drop-down arrow to change the ‘A’ to a ‘B’.
Find the ‘show leds’ block in the Basic section, add it to the ‘on button B pressed’ block, and select LEDs to draw a bus symbol.
Build the code - button B part 1:
↓

## Slide 33: Spicy 🌶️🌶️🌶️ Student Activity Steps 5
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘log data’ block and add it underneath. Add “bus” into the column circle and ‘1’ into the value circle. This will mean a 1 is added into the “bus” column when you press the button.
Build the code - button B part 2:
Find the ‘clear screen’ block in the Basic section and put it underneath.

## Slide 34: Spicy 🌶️🌶️🌶️ Student Activity Steps 6
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘on logo pressed’ block in the Input section and add it to your workspace.
Find the ‘show leds’ block in the Basic section, add it to the ‘on logo pressed’ block, and select LEDs to draw a truck symbol.
Build the code - logo pressed part 1:

## Slide 35: Spicy 🌶️🌶️🌶️ Student Activity Steps 7
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘log data’ block and add it underneath. Add “truck” into the column circle and ‘1’ into the value circle. This will mean a 1 is added into the “truck” column when you press the button.
Build the Code - logo pressed part 2:
Find the ‘clear screen’ block in the Basic section and put it underneath.
Test their code using the simulator and then download the code to their micro:bit.

## Slide 36: Spicy 🌶️🌶️🌶️ Student Activity Steps 8
Mild - Medium - Spicy 🌶️🌶️🌶️
Use your micro:bit to Collect Data:
Unplug the micro:bit and connect the battery pack.
Go to the predetermined observation area and start collecting data.
Collect data using the buttons to increase each count by 1. (Button A = cars, button B = buses, touch logo = trucks or vans.)
Pro tip: Students can press buttons A and B together to delete the log and start the survey again.

## Slide 37: Spicy 🌶️🌶️🌶️ Student Activity Steps 9
Mild - Medium - Spicy 🌶️🌶️🌶️
Disconnect the battery pack and plug the micro:bit back into a computer.
The MICROBIT drive will appear like a USB drive.
Look in the MICROBIT drive and open the MY_DATA file to see a table of your data in a web browser.
The times recorded in the table show the amount of time that passed since your micro:bit was powered on.
Paraphrase the data you have gathered.
↓

## Slide 38: Spicy 🌶️🌶️🌶️ Analyze Your Data 1
Mild - Medium - Spicy 🌶️🌶️🌶️
Students will paraphrase the traffic survey data collected using the data table that appears in a web browser.
Students can analyze their data using paper and pencil or a spreadsheet.
Use paper and pencil to add up the total of each column to make your own column or bar chart to visualize your survey data.

## Slide 39: Spicy 🌶️🌶️🌶️ Analyze Your Data 2
Mild - Medium - Spicy 🌶️🌶️🌶️
To use a spreadsheet, you can:
Press the copy button to copy the data so you can paste it straight into a spreadsheet.
Press the download button to download the data as a CSV (comma separated values) file, which you can also import into a spreadsheet.

## Slide 40: Spicy 🌶️🌶️🌶️ Code Details 1
Mild - Medium - Spicy 🌶️🌶️🌶️
This project uses the micro:bit’s data logging feature to record the number of cars, buses, and trucks.
When the program starts, the data logging table’s column headings are set as “car”, “bus”, and “truck”. A ‘yes’ icon appears on the LED display.
When you press button A, a ‘show leds’ block is used to display a symbol for a car and a ‘1’ is logged in the “car” column of your data table. The LED display is then cleared.

## Slide 41: Spicy 🌶️🌶️🌶️ Code Details 2
Mild - Medium - Spicy 🌶️🌶️🌶️
When you press button B, a ‘show leds’ block is used to display a symbol for a bus and a ‘1’ is logged in the “bus” column of your data table. The LED display is then cleared.
When you press the micro:bit’s touch logo, a ‘show leds’ block is used to display a symbol for a truck and a ‘1’ is logged in the “truck” column of your data table. The LED display is then cleared.

## Slide 42: Spicy 🌶️🌶️🌶️ Code Details 3
Mild - Medium - Spicy 🌶️🌶️🌶️
When you press buttons A and B at the same time, a skull icon appears on the micro:bit’s LED display, the log is cleared of data, and the data logging table’s column headings are reset. Then a ‘yes’ icon appears on the LED display to indicate that the micro:bit is ready to collect new data.

## Slide 43
Extension Ideas

## Slide 44: Traffic Survey Data Logger Extensions
Collect and compare data from different times of the day and suggest reasons why the data differs.
Make suggestions for how people could take better care of the environment using the data collected.
Make a graphical representation of the number of vehicles counted, for example, by using colored stickers.
Students could collect data by creating a paper and pen tally chart. How does this compare to using the micro:bit? Which method is more likely to be accurate?

## Slide 45
Renaming Column Headings

## Slide 46: Renaming Column Headings Step 1
Change the Column Heading Names:
Open the starter project at the appropriate spice level.
Explain that students have been provided starter code, which includes three column headings for “car”, “bus”, and “truck” and they are going to change these to “paper”, “plastic”, and “metal”.
This project uses the column headings “car”, “bus”, and “truck” in its data logging table.
You can tailor this project to best suit your class and the topics you are studying by changing the column headings. For example, you might want your students to collect data about different types of trash found in the playground. You could therefore change the column headings to “paper”, “plastic”, and “metal”.

## Slide 47: Renaming Column Headings Step 2
Find the ‘on start block’, which has a ‘set columns’ block inside it. Change the column headings inside this block to “paper”, “plastic”, and “metal”.
Find the ‘on button A + B pressed’ block, which has a ‘set columns’ block inside it. Change the column headings inside this block to “paper”, “plastic”, and “metal”.

## Slide 48: Renaming Column Headings Step 3
Find the set of blocks contained in ‘on button A pressed’ block. Find the ‘log data’ block and change the column heading “car” to “paper”. Edit the ‘show leds’ block to create an icon for paper.
Find the set of blocks contained in ‘on button B pressed’ block. Find the ‘log data’ block and change the column heading “bus” to “plastic”. Edit the ‘show leds’ block to create an icon for plastic.

## Slide 49: Renaming Column Headings Step 4
Find the set of blocks contained in ‘on logo pressed’ block. Find the ‘log data’ block and change the column heading “truck” to “metal”. Edit the ‘show leds’ block to create an icon for metal.