## Slide 1: What you need:
Project guide
Renewable Energy with Energy Light Meter
Integrating CS with Science - 4th Grade

## Slide 2: Renewable Energy with Energy Light Meter
Summary & Context
The BBC micro:bit has a light sensor on its LED display which can be used to collect light levels in a variety of locations around the learning environment.
Students can use the micro:bit energy light meter to combine light level data with their understanding of the Sun’s energy as a natural resource. This helps them explore how different energy sources and fuels affect the environment.
micro:bit Feature: Light Sensor
The micro:bit can be programmed to use its LED display as a light sensor. It measures light strength from 0 (no light) to 255 (the most intense light the micro:bit can measure).
Example: Students can measure light levels in different locations to explore how using natural light instead of electric lights affects the use of fuels and the environment.

## Slide 3: Computer Science Concepts
Inputs
Inputs allow computers to sense things happening in the real world so they can act on them and make something happen.
This project uses the light sensor and buttons for input.
The micro:bit has two buttons which can be programmed – buttons A and B. This project uses button A to measure light levels and store them in a variable. Button B is used to view the most recent measurement taken.
Storing Data
Variables store numbers or values that can change in a computer program.
We can describe variables as being like a box that stores information and which students can access, add to, or remove from at any time.
In computer science, a ‘string’ is a sequence of characters that can contain letters, numbers, symbols, and spaces.

## Slide 4: How the Energy Light Meter Works
The energy light meter uses a variable called “reading” to store the light level measured. It uses the micro:bit light sensor to store the light level in this variable when the program starts.
Students press button A each time they want to measure a light level.
Students press button B each time they want to view the most recent light level measured.
Using a variable to store the light level, rather than just displaying it, is helpful because students can take a light reading in a place where the display may be difficult to see, then wait to view the light measurement in a more convenient place.
Pro tip: Consider collecting light level data in different locations, both inside and outside the school building and throughout the day, to observe how location and time of day affect the data collected.

## Slide 5: Pick Your Level
Mild 🌶️ 30 mins | Learning outcome: I can collect light level data in various locations around my learning environment using the micro:bit energy light meter to explore how different energy sources can affect the Earth.
 | Activity description: Using existing code, measure light levels in different locations. Use the data to explore how natural resources provide energy and how energy use affects the environment.
Medium 🌶️🌶️ 45 mins | Learning outcome: I can modify my own energy light meter program to collect light level data in various locations around my learning environment to explore how different energy sources can affect the Earth.
 | Activity description: Modify the starter project to code your own energy light meter to measure light levels in different locations, then use the data to explore how natural resources provide energy and how energy use affects the environment.
Spicy 🌶️🌶️🌶️ 45-60 mins | Learning outcome: I can create my own energy light meter program to collect light level data in various locations around my learning environment to explore how different energy sources can affect the Earth.
 | Activity description: Code your own energy light meter program to measure light levels in different locations, then use the data to explore how natural resources provide energy and how energy use affects the environment.

## Slide 6
Mild

## Slide 7: Mild 🌶️ Introduction 1
Students will download the code on their micro:bit, connect the battery pack, measure the light level in various locations around the learning environment such as the classroom, building common spaces, and playground.
Consider collecting light level measurements in the same locations throughout the day. Teachers may wish to identify measurement spots in the classroom if results are being combined between students. Measurement spots should include areas that experience both natural light and shade throughout the day.
The micro:bit’s light sensor uses the display LEDs to measure light, so make sure the micro:bit’s LED display is pointing toward the light source. The light level reading will be a number between 0 (dark) and 255 (the most intense light the micro:bit can measure).
Mild 🌶️ - Medium - Spicy

## Slide 8: Mild 🌶️ Introduction 2
Students can use button B to display their light level reading, record it, and prepare to collect data at different locations.
  The 4th grade energy light meter recording sheet can be used to record the date, time, location, and species observation totals.
After collecting the data, students can create graphs to explore how natural resources provide energy and how energy use affects the environment.
Mild 🌶️ - Medium - Spicy
Pro tip: Variables hold only one value at a time. Students should record the location, time, and light level on a worksheet after each measurement.

## Slide 9: Mild 🌶️ Student Activity Steps
Open the project: mbit.io/us-lightmeter and download the code to the micro:bit.
Unplug the micro:bit and connect the battery pack.
Go to a measurement spot and start collecting data.
Collect light level data by pressing button A.
Press button B to show the light level data on the LED display.
Record the location, time, and light level on a worksheet.
Repeat data collection at different measurement spots and discuss location, time, and light level measurements. What do students notice and wonder about their results?
Mild 🌶️ - Medium - Spicy

## Slide 10: Mild 🌶️ Code Details
This project measures light level from 0 (darkest) to 255 (brightest).
Mild 🌶️ - Medium - Spicy
At the start of the program, the LED display shows “M” to signal that the micro:bit is ready to measure light levels, stores the initial light measurement in variable “reading”, and pauses for 100 ms before another input can happen.
Pressing button A measures the light level and stores it in variable “reading”. The LED display shows an animation to signal that a measurement was made and then waits half a second (500 ms) before showing “M” for measure.
Pressing button B will clear the screen, show the light level stored in the variable “reading” on the LED display, and wait half a second (500 ms) before showing “M” on the LED display.

## Slide 11
Medium

## Slide 12: Medium 🌶️🌶️ Introduction 1
Students open a starter project containing all the blocks they need to make the project.
Consider collecting light level measurements in the same locations throughout the day. Teachers may wish to identify measurement spots in the classroom if results are being combined between students. Measurement spots should include areas that experience both natural light and shade throughout the day.
The micro:bit’s light sensor uses the LEDs in its display to measure light, so make sure the micro:bit’s LED display is pointing toward the light source. The light level reading will be a number between 0 (dark) and 255 (the most intense light the micro:bit can measure).
Mild - Medium 🌶️🌶️ - Spicy

## Slide 13: Medium 🌶️🌶️ Introduction 2
Students can use button B to display their light level reading, record it, and prepare to collect data at a different measurement spot.
  The 4th grade energy light meter recording sheet can be used to record the date, time, location, and species observation totals.
After collecting the data, students can create graphs to support class discussion about how the apparent brightness of the sun compares to other stars based on their relative distances from Earth.
Mild - Medium 🌶️🌶️ - Spicy
Pro tip: Variables hold only one value at a time. Students should record the location, time, and light level on a worksheet after each measurement.

## Slide 14: Medium 🌶️🌶️ Student Activity Steps 1
Build the code - part 1:
Open the starter project: mbit.io/us-lightmeter-pp
Explain that students have all the code blocks they need.
Code the program to start with showing “M” for measure, set variable “reading” to store the light level measured, and pause for 100 ms before adding another input.
Make sure student code looks like:
Discuss the importance of accurate data and why it is helpful to pause before adding another input.
Mild - Medium 🌶️🌶️ - Spicy

## Slide 15: Medium 🌶️🌶️ Student Activity Steps 2
Build the code - part 2:
Code button A to measure the light level and store it in variable “reading”, show an animation to help students know a measurement was made, and then wait half a second (500 ms) before showing “M” for measure.
Make sure student code looks like:
Mild - Medium 🌶️🌶️ - Spicy

## Slide 16: Medium 🌶️🌶️ Student Activity Steps 3
Build the code - part 3:
Code button B to clear the screen, show the light level stored in variable “reading”, and wait half a second (500 ms) before showing “M” for measure.
Make sure student code looks like:
Test their code using the simulator and then download the code to their micro:bit.
Mild - Medium 🌶️🌶️ - Spicy

## Slide 17: Medium 🌶️🌶️ Student Activity Steps 4
Mild - Medium 🌶️🌶️ - Spicy
Use your micro:bit to collect data:
Unplug the micro:bit and connect the battery pack.
Go to a measurement spot and start collecting data.
Collect light level data by pressing button A.
Press button B on micro:bit to show the light level data on the LED display.
Record distance from the light source and light level on a worksheet.
Repeat data collection at different measurement spots and discuss location, time, and light level measurements. What do students notice and wonder about their results?

## Slide 18: Medium 🌶️🌶️ Code Details
This project measures light level from 0 (darkest) to 255 (brightest).
At the start of the program, the LED display shows “M” to signal that the micro:bit is ready to measure light levels, stores the initial light measurement in variable “reading”, and pauses for 100 ms before another input can happen.
Pressing button A measures the light level and stores it in variable “reading”. The LED display shows an animation to signal that a measurement was made and then waits half a second (500 ms) before showing “M” for measure.
Pressing button B will clear the screen, show the light level stored in the variable “reading” on the LED display, and wait half a second (500 ms) before showing “M” on the LED display.
Mild - Medium 🌶️🌶️ - Spicy

## Slide 19
Spicy

## Slide 20: Spicy 🌶️🌶️🌶️ Introduction 1
Mild - Medium - Spicy 🌶️🌶️🌶️
Students open Microsoft MakeCode and code their own energy light meter.
Consider collecting light level measurements in the same locations throughout the day. Teachers may wish to identify measurement spots in the classroom if results are being combined between students. Measurement spots should include areas that experience both natural light and shade throughout the day.
The micro:bit’s light sensor uses the LEDs in its display to measure light, so make sure the micro:bit’s LED display is pointing toward the light source. The light level reading will be a number between 0 (dark) and 255 (the most intense light the micro:bit can measure).

## Slide 21: Spicy 🌶️🌶️🌶️ Introduction 2
Mild - Medium - Spicy 🌶️🌶️🌶️
Students can use button B to display their light level reading, record it, and prepare to collect data at a different measurement spot.
  The 4th grade energy light meter recording sheet can be used to record the date, time, location, and species observation totals.
After collecting the data, students can create graphs to support class discussion about how the apparent brightness of the sun compares to other stars based on their relative distances from Earth.
Pro tip: Variables hold only one value at a time. Students should record the location, time, and light level on a worksheet after each measurement.

## Slide 22: Spicy 🌶️🌶️🌶️ Student Activity Steps 1
Build the code:
Open Microsoft MakeCode: microbit.makecode.org
Explain that students will use the toolbox to find code blocks.
Explain that students will need to code the three parts of the energy light meter:
  Code the program to show “M” for measure, set variable “reading” to store the light level measured, and pause for 100 ms on start.
  Code button A to measure the light level and store it in variable “reading”, show an animation to help students know a measurement was made, and then wait half a second (500 ms) before showing “M” for measure.
  Code button B to clear the screen, show the light level stored in variable “reading”, and wait half a second (500 ms) before showing “M” for measure.
Mild - Medium - Spicy 🌶️🌶️🌶️

## Slide 23: Spicy 🌶️🌶️🌶️ Student Activity Steps 2
Build the code - on start part 1:
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘show string’ block in the Basic section and update the string to read “M” to help students know the micro:bit is ready to measure light levels.
Select ‘Make a Variable’ in the Variables section. Name your variable “reading” because it will store the most recent light level recorded. You will see two new variable blocks appear.
Pro tip: Use variable names that describe the information that will be stored instead of using single letters like x, y, or z.

## Slide 24: Spicy 🌶️🌶️🌶️ Student Activity Steps 3
Build the code - on start part 2:
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘pause’ block in the Basic section to add a 100 ms pause before another input can happen.
Find the ‘set reading to 0’ block in the Variables section.
Find the ‘light level’ block in the Input section and put it on top of the 0 in ‘set reading to 0’ block. This will store the current light level reading in variable “reading”.

## Slide 25: Spicy 🌶️🌶️🌶️ Student Activity Steps 4
Build the code - button A part 1:
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘on button A pressed’ block in the Input section and add it to your workspace.
Find the ‘set reading to 0’ block in the Variables section.
Find the ‘light level’ block in the Input section and put it on top of the 0 in ‘set reading to 0’ block. This will store the current light level reading in variable “reading” when button A is pressed.

## Slide 26: Spicy 🌶️🌶️🌶️ Student Activity Steps 5
Build the code - button A part 2:
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘show icon’ block in the Basic section and select the arrow to the right of the heart icon image and select the small diamond icon.
Find the ‘show icon’ block in the Basic section and select the arrow to the right of the heart icon image and select the diamond icon.
Find the ‘show string’ block in the Basic section and update the string to read “M” to help students know the micro:bit is ready to measure light levels.

## Slide 27: Spicy 🌶️🌶️🌶️ Student Activity Steps 6
Build the code - button B part 1:
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘show number 0’ block in the Input section.
Find variable “reading” in the Variables section and put it on top of the 0 in ‘show number 0’ block.
Find the ‘on button A pressed’ block in the Input section and add it to your workspace. Select the down arrow and select B.
↓
Find the ‘clear screen’ block in the Basic section.

## Slide 28: Spicy 🌶️🌶️🌶️ Student Activity Steps 7
Build the code - button B part 2:
Test their code using the simulator and then download the code to their micro:bit.
Mild - Medium - Spicy 🌶️🌶️🌶️
Find the ‘pause’ block in the Basic section and click the arrow to update to time to half a second (500 ms).
Find the ‘show string’ block in the Basic section and update the string to read “M” to help students know the micro:bit is ready to measure light levels.

## Slide 29: Spicy 🌶️🌶️🌶️ Student Activity Steps 8
Mild - Medium - Spicy 🌶️🌶️🌶️
Use your micro:bit to collect data:
Unplug the micro:bit and connect the battery pack.
Go to a measurement spot and start collecting data.
Collect light level data by pressing button A.
Press button B to show the light level data on the LED display.
Record distance from the light source and light level on a worksheet.
Repeat data collection at different measurement spots and discuss location, time, and light level measurements. What do students notice and wonder about their results?

## Slide 30: Spicy 🌶️🌶️🌶️ Code Details
This project measures light level from 0 (darkest) to 255 (brightest).
At the start of the program, the LED display shows “M” to signal that the micro:bit is ready to measure light levels, stores the initial light measurement in variable “reading”, and pauses for 100 ms before another input can happen.
Pressing button A measures the light level and stores it in variable “reading”. The LED display shows an animation to signal that a measurement was made and then waits half a second (500 ms) before showing “M” for measure.
Pressing button B will clear the screen, show the light level stored in the variable “reading” on the LED display, and wait half a second (500 ms) before showing “M” on the LED display.
Mild - Medium - Spicy 🌶️🌶️🌶️

## Slide 31
Extension Ideas

## Slide 32: Energy Light Meter Extensions
Add a second micro:bit and radio functionality to allow remote reading of light levels.
If you have access to a light meter that measures light levels in other units, compare the micro:bit’s readings with it.
Measure light levels outside the building in both sunny and shaded areas to help students investigate how shade from buildings and trees can reduce the need for air conditioning.
Address standard 4-ESS3-2: Generate and compare multiple solutions to reduce the impacts of natural Earth processes on humans.*
  Students can design solutions to reduce human impacts on the Earth and use the micro:bit to collect data and compare their design solutions.
* integrate traditional science content with engineering through a Practice or Disciplinary Core Idea